MIDI SWITCHER / The information on this page is the bare minimum needed to build the project, however you will find more information at https://github.com/hotchk155/MIDI-Switcher/wiki. / I recommend you check the expanded instructions before you start building the board. / Here are the component designators used on the PCB: / C1,C2,C3 / C4 / C5 / D1 / D2 / R1 / R2,R3 / R4-R21 / LED1-8 / PWR, ACT / REG1 / MODE / ICSP / IC1 / IC2 / IC3, IC4 / MIDI_IN / DCIN, PORTA-H 100nF CERAMIC CAPACITOR (X3) / 47UF 63V ELECTROLYTIC CAPACITOR / 4U7 16V ELECTROLYTIC CAPACITOR / 1N4148 SIGNAL DIODE / 1N4001 RECTIFIER DIODE / 220R RESISTOR / 1K5 RESISTOR (X2) / 1K RESISTOR (X18) / BLUE 3MM LED (x8) / RED 3MM LED (x2) / 7805 +5V VOLTAGE REGULATOR TO220 / 6MM TACTILE SWITCH / 6 PIN SIL HEADER (OPTIONAL) / Please carefully check the polarity of D1, D2, REG1 and all LEDs before soldering! / PIC16F1825 MICROCONTROLLER / 6N138 OPTOCOUPLER / ULN2803A DARLINGTON DRIVER 8 CHANNEL (X2) / IC SOCKETS (x4) / When fitting IC3 please note that pin 1 notch is toward the bottom edge of the PCB / 5PIN DIN CONNECTOR FEMALE / STACKING DOUBLE TERMINAL BLOCK 5MM (X9) / Clip the terminal blocks into strips of four before soldering. Ensure the cable entry hole for each terminal faces the outside of the board! / Attach the 4 brass pillar “legs” into the holes in the PCB using the M3 machine screws / The default MIDI note to port mapping is / Port Note Port Note / PORT A C3 (60) PORT E E3 (64) / PORT B C#3 (61) PORT F F3 (65) / PORT C D3 (62) PORT G F#3 (66) / PORT D D#3 (63) PORT H G3 (67) / The default receive channel is MIDI Channel 1 for all ports. Output is set at 100% duty (i.e. constantly ON when triggered) and 20 milliseconds duration. / The configuration can be changed over MIDI using a downloadable Java application. Check the web link given at the top of this sheet for the full instruction manual and the application download. / * POWER THE BOARD FROM A DC SUPPLY OF 7-24 VOLTS / * DO NOT EXCEED 1A CURRENT DRAW PER PORT OR 3A CONTINUOUS FOR ALL PORTS COMBINED / * MAKE SURE YOUR POWER SUPPLY CAN PROVIDE SUFFICIENT CURRENT TO POWER YOUR COMBINED LOADS / * USE THE MARKINGS ON THE BOARD TO IDENTIFY THE LOCATION AND POLARITY OF EACH PORT. / * CHECK COMPONENTS AND POWER SUPPLY FOR SIGNS OF OVERHEATING DURING USE (REDUCE LOAD OR UPGRADE THE SUPPLY ACCORDINGLY) / * NEVER CONNECT THE BOARD DIRECTLY TO MAINS ELECTRICITY!!!!! / * ALWAYS CHECK THE MANUAL IF YOU HAVE ANY DOUBTS / * HAVE FUN! / Feel free to contact me at sixtyfourpixels@gmail.com with questions, suggestions and feedback.	MIDI SWITCHER / The information on this page is the bare minimum needed to build the project, however you will find more information at https://github.com/hotchk155/MIDI-Switcher/wiki. / I recommend you check the expanded instructions before you start building the board. / Here are the component designators used on the PCB: / C1,C2,C3 / C4 / C5 / D1 / D2 / R1 / R2,R3 / R4-R21 / LED1-8 / PWR, ACT / REG1 / MODE / ICSP / IC1 / IC2 / IC3, IC4 / MIDI_IN / DCIN, PORTA-H 100nF CERAMIC CAPACITOR (X3) / 47UF 63V ELECTROLYTIC CAPACITOR / 4U7 16V ELECTROLYTIC CAPACITOR / 1N4148 SIGNAL DIODE / 1N4001 RECTIFIER DIODE / 220R RESISTOR / 1K5 RESISTOR (X2) / 1K RESISTOR (X18) / BLUE 3MM LED (x8) / RED 3MM LED (x2) / 7805 +5V VOLTAGE REGULATOR TO220 / 6MM TACTILE SWITCH / 6 PIN SIL HEADER (OPTIONAL) / Please carefully check the polarity of D1, D2, REG1 and all LEDs before soldering! / PIC16F1825 MICROCONTROLLER / 6N138 OPTOCOUPLER / ULN2803A DARLINGTON DRIVER 8 CHANNEL (X2) / IC SOCKETS (x4) / When fitting IC3 please note that pin 1 notch is toward the bottom edge of the PCB / 5PIN DIN CONNECTOR FEMALE / STACKING DOUBLE TERMINAL BLOCK 5MM (X9) / Clip the terminal blocks into strips of four before soldering. Ensure the cable entry hole for each terminal faces the outside of the board! / Attach the 4 brass pillar “legs” into the holes in the PCB using the M3 machine screws / The default MIDI note to port mapping is / Port Note Port Note / PORT A C3 (60) PORT E E3 (64) / PORT B C#3 (61) PORT F F3 (65) / PORT C D3 (62) PORT G F#3 (66) / PORT D D#3 (63) PORT H G3 (67) / The default receive channel is MIDI Channel 1 for all ports. Output is set at 100% duty (i.e. constantly ON when triggered) and 20 milliseconds duration. / The configuration can be changed over MIDI using a downloadable Java application. Check the web link given at the top of this sheet for the full instruction manual and the application download. / * POWER THE BOARD FROM A DC SUPPLY OF 7-24 VOLTS / * DO NOT EXCEED 1A CURRENT DRAW PER PORT OR 3A CONTINUOUS FOR ALL PORTS COMBINED / * MAKE SURE YOUR POWER SUPPLY CAN PROVIDE SUFFICIENT CURRENT TO POWER YOUR COMBINED LOADS / * USE THE MARKINGS ON THE BOARD TO IDENTIFY THE LOCATION AND POLARITY OF EACH PORT. / * CHECK COMPONENTS AND POWER SUPPLY FOR SIGNS OF OVERHEATING DURING USE (REDUCE LOAD OR UPGRADE THE SUPPLY ACCORDINGLY) / * NEVER CONNECT THE BOARD DIRECTLY TO MAINS ELECTRICITY!!!!! / * ALWAYS CHECK THE MANUAL IF YOU HAVE ANY DOUBTS / * HAVE FUN! / Feel free to contact me at sixtyfourpixels@gmail.com with questions, suggestions and feedback.